# Tasar Rigging and Sailing Guide

## Rigging

- After signing out a boat, carefully transport all necessary equipment to the grassed rigging area (this will take multiple trips). When carrying the gear bag be careful to not let it fall to the ground as the daggerboard and rudder are extremely fragile.

- Check the hull for water by tilting the bow into the air. Afterwards, insert the stern plug and ensure the bailer is in the closed position.

### Rigging the Main Sail

- Connect the boom to the mast with shackles at gooseneck and outhaul.

- Thread the mainsheet through the mainsheet blocks and connect it to the boom. Tie a stopper knot at free end.

- Connect the boom vang and check the outhaul tension.

- Make certain that the whisker pole is connected.

- Connect the halyard and feed the mainsail into the mast track.  If wind conditions permit, raise the mainsail and connect the downhaul.  Otherwise, connect the downhaul after raising main just prior to launching.

- Lower the mainsail leaving the head in mast track.

### Rigging the Jib

- Connect the jib sheets to jib clew using the middle hole in the clew plate.

- Run the jib sheets through fairleads and tie a stopper knot.

- Connect the jib hanks to the forestay.  Connect the halyard to the jib by passing a loop through the cringle and then the ball through the loop.

- Raise the jib and connect the halyard tension line to the loop in the jib halyard.

- Adjust the luff tension so that it is “snug”.

- Connect the rudder to the transom.  Insert and secure the tiller and tiller extension.

### Rigging the Foils

- Raise the rudder blade upright and tie in place so that it won’t fall down onto the ground while the boat is being transported to the water.

- Stow a paddle and sponge in the front access port and ensure that the hand bailer is secured.

- You are now ready to get your gear on and start sailing!

## Launching

- Using the dolly, move the boat to a head-to-wind position near water’s edge.

- Make certain that the mainsheet and halyard are free and clear.  Hoist the main sail, lock the halyard in place, coil and stow it at base of mast.

- Check that the bailer is closed and stern plug is in.

- Always be mindful of the wind direction, dolly the boat into water until it floats free.  Immediately point the bow into the wind.  One of the crew takes the dolly back into the yard while the boat is on the water while the other crew hold the boat bow to wind.

- Ensure that there are no hazards or boats in your path.

- When ready to depart, point the bow across the wind (to close hauled). If the boat becomes unmanageable, pull the bow into the wind again. Step into the cockpit as the boat moves forward, and quickly do the following, in order:

- Pull the rudder downhaul line tight so that the rudder is set fully down into the water and then cleat it. An arm over the back of the boat sometimes helps this process.

- Carefully lift the daggerboard out of the cockpit and slide into the trunk.

- Determine your point of sail and adjust the main and jib sheets to the desired trim.

## Tacking

Before tacking, check that the new intended direction is clear. Head up and sheet in to a close hauled course, while still maintaining your speed. Smoothly, push the tiller away from you. As the boat steers through the wind, cross the cockpit to the new windward side. The crew will sheet the jib onto the new side as the bow comes through the wind.  The skipper will reach behind their back, with mainsheet in hand, to switch hands on the tiller extension. Establish a new point of sail.

## Gybing

Before gybing, check that the new intended direction is clear. Harden up the main sheet.  When ready, the skipper pulls the tiller towards them.  As the stern of the boat is moving through the wind, grab the mainsheet line just under the boom and pull in the slack. (Note that if the mainsheet is slack, there is a tendency for it to get caught on the edge of the stern.) At the same time, pull the boom across the boat, preventing it from snapping across. Establish a new point of sail and ease the mainsheet to the desired trim.

## Returning to Shore

- Choose an area on the shore to land and ease out the mainsheet as you approach to reduce speed.

- Release the rudder downhaul about 100 feet out from shore and prepare to raise the daggerboard.

- When close to the shore, raise the daggerboard and lay it across the deck above the trunk.

- While still in a few feet of water turn the bow into the wind.  The crew steps out and holds the bow into the wind.  The skipper lifts the rudder fully and removes the mainsheet.

- The skipper then retrieves the dolly from the yard.  Float the boat onto the dolly and transport the boat to the yard for washing and de rigging.  In high winds, lower the mainsail while rolling the boat up the ramp.

## De-rigging

- Proceed to the rigging area and thoroughly wash the boat, foils, lines and fittings with fresh water.  Pay particular attention to the cockpit drain – ensure that it is clear of sand and left open.

- If the sail is wet from a capsize or sea spray make sure to wash it also and allow to dry.

- Check the hull for water by tilting the bow into the air and removing the stern plug.

- Once rinsed, carefully place the daggerboard, rudder and tiller in gear bag head first. This ensures the fragile tips are less likely to be damaged.

- Coil the mainsheet and run the gear bag snap strap through the top.

- Roll the main sail and jib, place them in their respective bags and stow in the club room.

- Disconnect the vang and main sheet from the boom and remove it from the gooseneck.  Stow the boom in the club room.

- Don't forget to sign back in!

## Racing

Want to take your sailing to the next level? Racing against fellow Tasar sailors is a great way to improve your skills. JSCA has an active Tasar racing fleet which frequently sees 10+ boats joining in the well organized races on a Sunday afternoon or Tuesday night.

Want to know more? Whether you are new to racing or a seasoned pro, the Rookie Racing seminar includes information on how the races are run 'JSCA style' and some basic tactics and tricks for making the best of the often challenging conditions. JSCA hosts the seminar on the dates listed below:

|  | May 16th @ 09:00 |  |  |
| --- | --- | --- | --- |
|  | July 11th @ 09:00 |  |  |

For the full 2009 event schedule please visit --> http://www.jsca.bc.ca/calandar.html

## Clinic Checklist

### Preparation:

- Sign-out process

- Boat inspection

- Rigging

- Capsizing discussion: reasons why and how to avoid

### Sailing Skills:

- Launching

- Tacking

- Gybing

- Right from inverted position

- Returning to Shore

### Back on land:

- Cleaning

- Derigging

- Folding of sails

- Storage

### Privileges:

- RECREATION - You may sail Tasars once you have passed the clinic.

- RACING - You may race Tasars after passing the clinic and attending the Rookie Racing Seminar.